  Lista podstawowych parametrow pomiaru wydajnosci jednostek funkcjonalych
  “Uncore” (LLC controller,Memory controllers,UPI Link controller,II/O controller)
  procesorow: SkyLake-X I Cascade_Lake.

- UNC_CHA_TOR_INSERTS.IO_HIT ← Hits from local I/O devices (possibly GPU)
- UNC_CHA_TOR_INSERTS.IO_MISS ← Misses from local I/O devices (possibly GPU)
- UNC_CHA_TOR_INSERTS.IA ← Local Cores inserts to Table-Of-Requests
- UNC_CHA_TOR_INSERTS.IA_HIT ← Local Cores inserts that hit (LLC slice) (Important event)
- UNC_CHA_TOR_INSERTS.IA_MISS ← Local Cores inserts that miss (LLC slice) (Important event)
- UNC_CHA_TOR_OCCUPANCY.IA_HIT ← TOR number of entries scored hit (informative event)
- UNC_CHA_TOR_OCCUPANCY.IA_MISS ← TOR number of entries scored miss (informative event)
- UNC_CHA_CLOCKTICKS ← Important event
- UNC_CHA_IMC_READS_COUNT.NORMAL
- UNC_CHA_MISC.RFO_HIT_S
- UNC_CHA_REQUESTS.READS ← Important event
- UNC_CHA_REQUESTS.WRITES ← Important event
- UNC_CHA_REQUESTS.READS_LOCAL ← Important event
- UNC_CHA_REQUESTS.WRITES_LOCAL ← Important event
- UNC_CHA_SF_EVICTION.M_STATE ← Informative event (Snoop Filter)
- UNC_CHA_SF_EVICTION.E_STATE ← Informative event (Snoop Filter)
- UNC_CHA_SF_EVICTION.S_STATE ← Informative event (Snoop filter)
- UNC_CHA_LLC_VICTIMS.TOTAL_M ← Important event (LLC cache line “Modified” victimized on fill)
- UNC_CHA_LLC_VICTIMS.TOTAL_E ← Important event (Total number of lines victimized)
- UNC_CHA_LLC_VICTIMS.TOTAL_S ← Important event (Total number of lines victimized)
- UNC_CHA_LLC_VICTIMS.TOTAL_F ← Important event (Total number of lines victimized)
- UNC_CHA_TOR_INSERTS.IA_HIT_DRD ← Important event (Core insertion demand data read scored LLC hit)
- UNC_CHA_TOR_INSERTS.IA_MISS_DRD ← Important event (Core insertion demand data read scored LLC miss)
- UNC_CHA_TOR_OCCUPANCY.IA_HIT_DRD ← Important event (Core insertion demand data read scored LLC hit – TOR occupancy)
- UNC_CHA_TOR_OCCUPANCY.IA_MISS_DRD ← Important event (Core insertion demand data read scored LLC miss – TOR occupancy)
- UNC_IIO_CLOCKTICKS ← Important event (II/O clock)
- UNC_IIO_DATA_REQ_BY_CPU.MEM_WRITE.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every write request of 4 bytes of data made to the MMIO space of a card on IIO Part0 by a unit on the main die (generally a core) or by another IIO unit. In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.MEM_WRITE.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every write request of 4 bytes of data made to the MMIO space of a card on IIO Part1 by a unit on the main die (generally a core) or by another IIO unit. In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus.",
- UNC_IIO_DATA_REQ_BY_CPU.MEM_WRITE.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every write request of 4 bytes of data made to the MMIO space of a card on IIO Part2 by a unit on the main die (generally a core) or by another IIO unit. In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.MEM_WRITE.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every write request of 4 bytes of data made to the MMIO space of a card on IIO Part3 by a unit on the main die (generally a core) or by another IIO unit. In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus
- UNC_IIO_DATA_REQ_BY_CPU.PEER_WRITE.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of 4 bytes of data made to the MMIO space of a card on IIO Part0 by a different IIO unit. Does not include requests made by the same IIO unit. In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.PEER_WRITE.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of 4 bytes of data made to the MMIO space of a card on IIO Part1 by a different IIO unit. Does not include requests made by the same IIO unit. In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.PEER_WRITE.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of 4 bytes of data made to the MMIO space of a card on IIO Part2 by a different IIO unit. Does not include requests made by the same IIO unit. In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus
- UNC_IIO_DATA_REQ_BY_CPU.PEER_WRITE.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of 4 bytes of data made to the MMIO space of a card on IIO Part3 by a different IIO unit. Does not include requests made by the same IIO unit. In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.MEM_READ.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every read request for 4 bytes of data made by a unit on the main die (generally a core) or by another IIO unit to the MMIO space of a card on IIO Part0. In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.MEM_READ.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every read request for 4 bytes of data made by a unit on the main die (generally a core) or by another IIO unit to the MMIO space of a card on IIO Part1. In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.MEM_READ.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every read request for 4 bytes of data made by a unit on the main die (generally a core) or by another IIO unit to the MMIO space of a card on IIO Part2. In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.MEM_READ.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every read request for 4 bytes of data made by a unit on the main die (generally a core) or by another IIO unit to the MMIO space of a card on IIO Part3. In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.PEER_READ.PART0 ← Important event (PCIE-GPU, NIC)
  Counts ever peer to peer read request for 4 bytes of data made by a different IIO unit to the MMIO space of a card on IIO Part0. Does not include requests made by the same IIO unit. In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.PEER_READ.PART1 ← Important event (PCIE-GPU, NIC)
  Counts ever peer to peer read request for 4 bytes of data made by a different IIO unit to the MMIO space of a card on IIO Part1. Does not include requests made by the same IIO unit. In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.PEER_READ.PART2 ← Important event (PCIE-GPU, NIC)
  Counts ever peer to peer read request for 4 bytes of data made by a different IIO unit to the MMIO space of a card on IIO Part2. Does not include requests made by the same IIO unit. In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_BY_CPU.PEER_READ.PART3 ← Important event (PCIE-GPU, NIC)
  Counts ever peer to peer read request for 4 bytes of data made by a different IIO unit to the MMIO space of a card on IIO Part3. Does not include requests made by the same IIO unit. In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus
- UNC_IIO_DATA_REQ_OF_CPU.MEM_WRITE.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every write request of 4 bytes of data made by IIO Part0 to a unit onthe main die (generally memory). In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.MEM_WRITE.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every write request of 4 bytes of data made by IIO Part1 to a unit on the main die (generally memory). In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.MEM_WRITE.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every write request of 4 bytes of data made by IIO Part2 to a unit on the main die (generally memory). In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus
- UNC_IIO_DATA_REQ_OF_CPU.MEM_WRITE.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every write request of 4 bytes of data made by IIO Part3 to a unit on the main die (generally memory). In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.PEER_WRITE.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of 4 bytes of data made by IIO Part0 to the MMIO space of an IIO target. In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.PEER_WRITE.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of 4 bytes of data made by IIO Part1 to the MMIO space of an IIO target. In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.PEER_WRITE.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of 4 bytes of data made by IIO Part2 to the MMIO space of an IIO target. In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.PEER_WRITE.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of 4 bytes of data made by IIO Part3 to the MMIO space of an IIO target. In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus
- UNC_IIO_DATA_REQ_OF_CPU.MEM_READ.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every read request for 4 bytes of data made by IIO Part0 to a unit on the main die (generally memory). In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.MEM_READ.PART1 ← Important event (PCIE-GPU, NIC)
- Counts every read request for 4 bytes of data made by IIO Part1 to a unit on the main die (generally memory). In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.MEM_READ.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every read request for 4 bytes of data made by IIO Part2 to a unit on the main die (generally memory). In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus
- UNC_IIO_DATA_REQ_OF_CPU.MEM_READ.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every read request for 4 bytes of data made by IIO Part3 to a unit on the main die (generally memory). In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus
- UNC_IIO_DATA_REQ_OF_CPU.PEER_READ.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer read request for 4 bytes of data made by IIO Part0 to the MMIO space of an IIO target. In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.PEER_READ.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer read request for 4 bytes of data made by IIO Part1 to the MMIO space of an IIO target. In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus.
- UNC_IIO_DATA_REQ_OF_CPU.PEER_READ.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer read request for 4 bytes of data made by IIO Part2 to the MMIO space of an IIO target. In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus
- UNC_IIO_DATA_REQ_OF_CPU.PEER_READ.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer read request for 4 bytes of data made by IIO Part3 to the MMIO space of an IIO target. In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus
- UNC_IIO_TXN_REQ_BY_CPU.MEM_WRITE.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every write request of up to a 64 byte transaction of data made to the MMIO space of a card on IIO Part0 by a unit on the main die (generally a core) or by another IIO unit. In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus
- UNC_IIO_TXN_REQ_BY_CPU.MEM_WRITE.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every write request of up to a 64 byte transaction of data made to the MMIO space of a card on IIO Part1 by a unit on the main die (generally a core) or by another IIO unit. In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus.
- UNC_IIO_TXN_REQ_BY_CPU.MEM_WRITE.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every write request of up to a 64 byte transaction of data made to the MMIO space of a card on IIO Part2 by a unit on the main die (generally a core) or by another IIO unit. In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus.
- UNC_IIO_TXN_REQ_BY_CPU.MEM_WRITE.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every write request of up to a 64 byte transaction of data made to the MMIO space of a card on IIO Part3 by a unit on the main die (generally a core) or by another IIO unit. In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus
- UNC_IIO_TXN_REQ_BY_CPU.PEER_WRITE.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of up to a 64 byte transaction of data made to the MMIO space of a card on IIO Part0 by a different IIO unit. Does not include requests made by the same IIO unit. In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus
- UNC_IIO_TXN_REQ_BY_CPU.PEER_WRITE.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of up to a 64 byte transaction of data made to the MMIO space of a card on IIO Part1 by a different IIO unit. Does not include requests made by the same IIO unit. In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus
- UNC_IIO_TXN_REQ_BY_CPU.PEER_WRITE.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of up to a 64 byte transaction of data made to the MMIO space of a card on IIO Part2 by a different IIO unit. Does not include requests made by the same IIO unit. In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus.
  UNC_IIO_TXN_REQ_BY_CPU.PEER_WRITE.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer write request of up to a 64 byte transaction of data made to the MMIO space of a card on IIO Part3 by a different IIO unit. Does not include requests made by the same IIO unit. In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus.
- UNC_IIO_TXN_REQ_OF_CPU.MEM_READ.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every read request for up to a 64 byte transaction of data made by IIO Part0 to a unit on the main die (generally memory). In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_TXN_REQ_OF_CPU.MEM_READ.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every read request for up to a 64 byte transaction of data made by IIO Part1 to a unit on the main die (generally memory). In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus
- UNC_IIO_TXN_REQ_OF_CPU.MEM_READ.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every read request for up to a 64 byte transaction of data made by IIO Part2 to a unit on the main die (generally memory). In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus.
- UNC_IIO_TXN_REQ_OF_CPU.MEM_READ.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every read request for up to a 64 byte transaction of data made by IIO Part3 to a unit on the main die (generally memory). In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus
- UNC_IIO_TXN_REQ_OF_CPU.PEER_READ.PART0 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer read request of up to a 64 byte transaction made by IIO Part0 to the MMIO space of an IIO target. In the general case, Part0 refers to a standard PCIe card of any size (x16,x8,x4) that is plugged directly into one of the PCIe slots. Part0 could also refer to any device plugged into the first slot of a PCIe riser card or to a device attached to the IIO unit which starts its use of the bus using lane 0 of the 16 lanes supported by the bus.
- UNC_IIO_TXN_REQ_OF_CPU.PEER_READ.PART1 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer read request of up to a 64 byte transaction made by IIO Part1 to the MMIO space of an IIO target. In the general case, Part1 refers to a x4 PCIe card plugged into the second slot of a PCIe riser card, but it could refer to any x4 device attached to the IIO unit using lanes starting at lane 4 of the 16 lanes supported by the bus
- UNC_IIO_TXN_REQ_OF_CPU.PEER_READ.PART2 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer read request of up to a 64 byte transaction made by IIO Part2 to the MMIO space of an IIO target. In the general case, Part2 refers to a x4 or x8 PCIe card plugged into the third slot of a PCIe riser card, but it could refer to any x4 or x8 device attached to the IIO unit and using lanes starting at lane 8 of the 16 lanes supported by the bus
- UNC_IIO_TXN_REQ_OF_CPU.PEER_READ.PART3 ← Important event (PCIE-GPU, NIC)
  Counts every peer to peer read request of up to a 64 byte transaction made by IIO Part3 to the MMIO space of an IIO target. In the general case, Part3 refers to a x4 PCIe card plugged into the fourth slot of a PCIe riser card, but it could brefer to any device attached to the IIO unit using the lanes starting at lane 12 of the 16 lanes supported by the bus.
- Less informative events
- UNC_IIO_TXN_REQ_OF_CPU.PEER_WRITE.PART0
- UNC_IIO_TXN_REQ_OF_CPU.PEER_WRITE.PART1
- UNC_IIO_TXN_REQ_OF_CPU.PEER_WRITE.PART2
- UNC_IIO_TXN_REQ_OF_CPU.PEER_WRITE.PART3
- UNC_IIO_TXN_REQ_BY_CPU.PEER_READ.PART0
- UNC_IIO_TXN_REQ_BY_CPU.PEER_READ.PART1
- UNC_IIO_TXN_REQ_BY_CPU.PEER_READ.PART2
- UNC_IIO_TXN_REQ_BY_CPU.PEER_READ.PART3
- UNC_M_WPQ_OCCUPANCY
- UNC_M_WPQ_INSERTS
- UNC_M_POWER_SELF_REFRESH
- UNC_M_CLOCKTICKS ← Important event